## Slide 1
How Much Contamination Is Here?
SR 132 Modesto Soil Stockpiles · Stanislaus County, CA · Site Code 900259
COMMUNITY BRIEFING
72,000 mg/kg
Highest barium level ever found in soil
(Stockpile 3, 2006 investigation)
~14× over limit
That peak is about 14 times the
residential safety threshold (5,200 mg/kg)
22 years
of testing and regulatory oversight
by DTSC, 2004–2026
Maximum Barium Found (2006) vs. Safety Thresholds
Chart: 
| Stockpile 1 | Stockpile 2 | Stockpile 3 | Residential limit | Industrial limit
Barium (mg/kg) | 130 | 64000 | 72000 | 5200 | 63000
Bars = actual soil test results. Gray bars = the health-based safety limits DTSC compares them to.
What else was found?
● Lead
Present at modest levels alongside barium; contained in the same capped area.
● Chromium & Cadmium
Investigated closely — never confirmed as significant soil contaminants here.
● Petroleum residue (TPH) & PAHs
One sample tested; results were below health-based limits.
CHHSL = California Human Health Screening Level, the health-based soil standard set by DTSC to protect residents. Source: DTSC/Caltrans site record (Site Code 900259).

## Slide 2
Is It Dangerous? Health Risks & Is It Spreading?
SR 132 Modesto Soil Stockpiles · Stanislaus County, CA · Site Code 900259
COMMUNITY BRIEFING
🔒
Soil Contact
CONTAINED
Barium-containing soil is capped and fenced under a highway embankment, with a permanent deed restriction (2024) blocking future digging or residential use.
💧
Groundwater
NOT REACHING DRINKING WATER
Monitored 2012–2023. Barium, lead, chromium, beryllium, and arsenic never exceeded safe drinking-water limits in any well, any year.
🔍
Ongoing Oversight
ACTIVELY MONITORED
DTSC requires five-year site reviews starting 2028. The deed restriction is permanent — it does not expire when monitoring ends.
The One Real Exceedance: Nitrate in Groundwater
Chart: 
| May 2012 | Sep 2012 | Nov 2012 | Mar 2013
MW-5 (nearest stockpiles) | 26 | 22 | 24 | 30
MW-1 (upgradient/background) | 12 | 12 | 12 | 13
Safety limit (MCL) | 10 | 10 | 10 | 10
Both wells stay above the limit — even MW-1, upgradient of the stockpiles — pointing to regional farm-fertilizer background, not this site. This groundwater is not a drinking source.
Health Impacts at a Glance
Substance | Main health concern | Unsafe here?
Barium | Heart rhythm & blood pressure at high exposure | No
Lead | No safe exposure level, especially for children | No
Nitrate | “Blue baby syndrome” in infants under 6 months | GW only¹
Chromium / Cadmium | Cancer risk at high exposure | No
¹ Nitrate exceeds the limit in groundwater, which is not used as a drinking source at this site.
Bottom line: DTSC's official risk assessments found health risks at this site far below the level of regulatory concern — largely because the contamination is contained, monitored, and not reaching drinking water.